CZTI Noise Reduction Processing Document
Mayuri Shinde
Jan 24,2018

Installation :

1. Install the new version of pipeline in your system.
2. If you have the configured ~/.bashrc file for the old pipeline, then
•Comment the old as1czt variable's path.
•Add following line to ~/.bashrc file
export as1czt={Path up to the new pipeline folder}/czti_pipeline/czti/
3. Add following Path for Noise_Cleaning to ~/.bashrc file
export CZTNOISECLEAN=<noise_basedir>
export PATH="$PATH:${CZTNOISECLEAN}/bin/"
Example:
export CZTNOISECLEAN=/home/cztipoc//noise_codes/
export PATH="$PATH:${CZTNOISECLEAN}/bin/"
4. Execute following commands in terminal
source ~/.bashrc
cd $as1czt
cd ../
./InstallLibs
cd $as1czt
make
cd scripts
chmod +x cztpipeline
cd $CZTNOISECLEAN
make

Prerequisite :
1. gcc compiler
2. cfitsio installation

All Threshold files will be available in config directory of noise_code
3. saaThreshold.txt
4. noiseReductionThreshold.txt
5. Det_thresholdlld.txt
6. pix_thresholdlld.txt
7. CALDB badpix file and CALDB lld file
(Path : /data2/czti/public_package/CALDB/data/as1/czti/bcf/)

For orbit data:
8. mkf file path :	/data2/czti/level2/<observationid_of_specific_orbit>/czti/orbit/<orbit_number>/ (.mkf)
9. Event file path : /data2/czti/level2/<observationid_of_specific_orbit>/czti/orbit/<orbit_number>/modeM0/ (cztM0_level2.evt)

  For merge data :
8. mkf file path : /data2/czti/level2/<observationid_of_specific_orbit>/czti/ (.mkf)
9. Event file path : /data2/czti/level2/<observationid_of_specific_orbit>/czti/modeM0/ (cztM0_level2.evt)

1.Data selection :
Input files -
1. MKF file
2. SAA configuration file(saaThreshold.txt)
3. Event file(Output event file of cztpha2energy)

Output files -
SAA removed event file/list of files(if orbit contain 2 SAA then number of output files will be 3 according to SAA position)

Output file name will be _0.evt , _1.evt etc.

How to compile -
gcc cztdataselection.c -o cztdataselection -I<path_of_the_cfitsio_include_directory> -L<path_of_the_cfitsio_lib_directory> -lcfitsio -lm

Example :
gcc cztdataselection.c -o cztdataselection -I$as1czt/include -L$as1czt/lib -lcfitsio -lm

How to run -
<cztdataselection executable file> mkf_file SAA_CONFIG_FILE event_file

Example :
cztdataselection AS1A02_174T04_9000000938_06835czt_level2.mkf saaThreshold AS1A02_174T04_9000000938_06835cztM0_level2.evt

2.Noisy Pixel Cleaning :
Input files -
1. SAA removed event file (output of cztdataselection)
2. CALDB Badpix file
3. Configuration file (noiseReductionThreshold.txt)

Output files -
1. Noise Cleaned Level 2 event file(_0_nc.evt , _1_nc.evt etc.)
2. Bad pixel file(0_badpix_nc.fits)

How to compile -
gcc cztnoisypixclean.c -o cztnoisypixclean -I<path_of_the_cfitsio_include_directory> -L<path_of_the_cfitsio_lib_directory> -lcfitsio -lm

Example :
gcc cztnoisypixclean.c -o cztnoisypixclean -I$as1czt/include -L$as1czt/lib -lcfitsio -lm

How to run -
<cztnoisypixclean executable file> output_file_of_cztdataselection caldb_badpix_file bunch_file CONFIG_FILE

Example :
cztnoisypixclean AS1A02_174T04_9000000938_06833cztM0_level2_0.evt AS1cztbadpix20160809v01.fits noiseReductionThreshold.txt

3.Super Bunch Cleaning
Input files -
1. Noise Cleaned Level 2 event file(output of noisy pixel clean)
2. Bunch file
3. Livetime file(generated by bunchclean module of cztpipeline)

Output files -
1. Super bunch cleaned level 2 event file(_0_nc_sbc.evt , _1_nc_sbc.evt etc.)
2. Bad time interval file(_bti.fits)
    3. Corrected livetime file(sbc_livetime.fits)

How to compile -
gcc cztsuperbunchclean.c -o cztsuperbunchclean -I<path_of_the_cfitsio_include_directory> -L<path_of_the_cfitsio_lib_directory> -lcfitsio -lm

Example :
gcc cztsuperbunchclean.c -o cztsuperbunchclean -I$as1czt/include -L$as1czt/lib -lcfitsio -lm

How to run -
< cztsuperbunchclean executable file> output_event_file_of_noisy_pix_clean bunch_file
livetime_file orbit_number

Example :
cztsuperbunchclean AS1A02_174T04_9000000938_06835cztM0_level2_0_nc.evt AS1A02_174T04_9000000938_06833cztM0_level2_bunch.fits livetime.fits 06835

4.Heavy bunch cleaning
Input files -
1. Super bunch cleaned Level 2 event file(output of super bunch clean)
2. Bunch file
3. CALDB lld threshold file

Output files -
1. Heavy bunch cleaned level 2 event file(_0_nc_sbc_hbc.evt , _1_nc_sbc_hbc.evt etc.)
How to compile -
gcc cztheavybunchclean.c -o cztheavybunchclean -I<path_of_the_cfitsio_include_directory> -L<path_of_the_cfitsio_lib_directory> -lcfitsio -lm

Example :
gcc cztheavybunchclean.c -o cztheavybunchclean -I$as1czt/include -L$as1czt/lib -lcfitsio -lm

How to run -
< cztheavybunchclean executable file> output_file_of_super_heavy_bunch_clean bunch_file lld_file

Example :
cztheavybunchclean AS1A02_174T04_9000000938_06835cztM0_level2_0_nc_sbc.evt AS1A02_174T04_9000000938_06833cztM0_level2_bunch.fits AS1cztlld20160517v01.fits

5.Flickering Pixel Cleaning :
Input files -
1. Heavy bunch cleaned level 2 event file (output of heavy bunch clean)
2. Badpix file(output badpix of noisy pix clean)

Output files -
1. Flickering pixel Cleaned Level 2 event file(_0_nc_sbc_hbc_fc.evt , _1_nc_sbc_hbc_fc .evt etc.)
2. Updated bad pixel file(0_badpix_nc_fc.fits)
3. Pixel BTI file(0_nc_sbc_hbc_fc.bti)

How to compile -
gcc cztflickpixclean.c -o cztflickpixclean -I<path_of_the_cfitsio_include_directory> -L<path_of_the_cfitsio_lib_directory> -lcfitsio -lm

Example :
gcc cztflickpixclean.c -o cztflickpixclean -I$as1czt/include -L$as1czt/lib -lcfitsio -lm

How to run -
< cztflickpixclean executable file> output_event_file_of_heavy_bunch_clean output_badpix_file_of_noisypix_clean

Example :
cztflickpixclean AS1A02_174T04_9000000938_06833cztM0_level2_0_nc_sbc_hbc.evt AS1A02_174T04_9000000938_06833cztM0_level2_0_badpix_nc.fits

6.LLD cut off :
Input files -
1. Flickering pixel cleaned level 2 event file (output of flickering pixel clean)
2. CALDB lld threshold file
3. Detector threshold file(Det_thresholdlld.txt)
4. Pixel threshold file(pix_thresholdlld.txt)

Output files -
1. After lld cut off Level 2 event file(fc_lldcut.evt etc.)

How to compile -
gcc cztlldcutoff.c -o cztlldcutoff -I<path_of_the_cfitsio_include_directory> -L<path_of_the_cfitsio_lib_directory> -lcfitsio -lm

Example :
gcc cztlldcutoff.c -o cztlldcutoff -I$as1czt/include -L$as1czt/lib -lcfitsio -lm

How to run -
< cztlldcutoff executable file> output_event_file_of_flickering_pix_clean lld_thresh_file Det_thresholdlld.txt pix_thresholdlld.txt

Example :
cztlldcutoff AS1A02_174T04_9000000938_06833cztM0_level2_0_nc_sbc_hbc_fc.evt AS1cztlld20160517v01.fits Det_thresholdlld.txt pix_thresholdlld.txt

7.Event seperation :
Input files -
1. Event file (output of lld cut off)

Output files -
1. Single Event file (_single.evt)
2. Double Event file (_double.evt)

How to compile -
gcc czteventsep.c -o czteventsep -I<path_of_the_cfitsio_include_directory> -L<path_of_the_cfitsio_lib_directory> -lcfitsio -lm

Example :
gcc czteventsep.c -o czteventsep -I$as1czt/include -L$as1czt/lib -lcfitsio -lm

How to run -
< czteventsep executable file> output_event_file_of_lld_cut_off

Example :
czteventsep AS1A02_174T04_9000000938_06833cztM0_level2_0_nc_sbc_hbc_fc_lldcut.evt

clean_data.sh

You can run all the noise cleaning modules using clean_data.sh script.

The input files required for clean_data.sh are:
i. MKF File with Path
ii. saaThreshold text file with Path from config directory
iii. Event File after pha2energy
iv. Badpix file from CALDB directory
v. Bunch fits file
vi. noiseReductionThreshold file from config directory
vii. LLD file from CALDB directory
viii. Mkf threshold file

How to run clean_data.sh :

clean_data.sh {MKF File} {SAAThreshold File} {.evt file} {caldb_badpix file} {bunch.fits}
{noiseReductionThreshold file} {caldb_lld file} {MKF threshold file}

Example:
 clean_data.sh /data2/czti/level2/20170102_G06_135T03_9000000944_level2/czti/AS1G06_135T03_9000000944czt_level2.mkf /home/cztipoc/czti_svn/trunk/users/mayuri/noise_codes/config/saaThreshold.txt /data2/czti/level2/20170102_G06_135T03_9000000944_level2/czti/modeM0/AS1G06_135T03_9000000944cztM0_level2.evt /home/cztipoc/CALDB/data/as1/czti/bcf/AS1cztbadpix20160908v01.fits /data2/czti/level2/20170102_G06_135T03_9000000944_level2/czti/modeM0/AS1G06_135T03_9000000944cztM0_level2_bunch.fits /home/cztipoc/czti_svn/trunk/users/mayuri/noise_codes/config/noiseReductionThreshold.txt /home/cztipoc/CALDB/data/as1/czti/bcf/AS1cztlld20160517v01.fits /home/cztipoc/czti_svn/trunk/users/ajay/pipeline/CZTI/czti/paramfiles/mkfThresholds.txt